## Slide 1
Call Forward
● Lift handset.
● Dial 7 5 4 .
● Dial the desired call forward number.
0 - For unconditional, 1 - For no answer calls,
2 - For busy calls,
3 - For busy/no answer calls,
4 - Follow me,
5 - Off-net (Forward to outside)
(In GHX-308A, just unconditional call forward is
available. You need not dial the call forward type no.)
● If you want forward number 1-4, dial the extension
number receiving calls. (If you select forward type
5, dial telephone number to be forwarded and
make hook flash.)
● Hang up.
● To cancel Call Forward, lift handset and dial 7 5 4.
● Hang up.
Queuing
If you access a busy line, you may request the system
to place you on hold until the next line becomes idle.
● Lift handset.
● Dial busy line. (Busy tone is heard.)
● Dial 7 5 6 . (Confirmation tone is heard.)
● Hang up.
Storing Station Speed Dial Numbers
● Lift handset.
● Dial 7 5 5 .
● Dial speed dial number bin.
(00~09 : 36/46, 00-19 : 308A/616)
● Dial speed dial number you wish to store.
● Briefly press and release the hook switch.
(Confirmation tone is heard.)
Using Speed Dial
● Lift handset.
● Dial 7 5 * or 7 5 8.
● Dial the desired speed number bin.
(00~09 : 36/46, 00-19 : 308A/616)
● Hang up.
Placing a Call Wait
After receiving intercom busy tone,
● Briefly press and release the hook switch.
● Dial 3 .
● When the called party answers, consult with them.
Receiving a Call Wait
● Receive call wait warning tone by handset.
● Hang up on the present call to take a new one, or
ignore the call wait signal.
Placing an Outside Call
● Lift handset.
● Dial appropriate access code.
308A : 9, 81~83 or 8801~8803
36 : 9, 81~87 or 8801~8812
46 : 9, 81~87 or 8801~8814
616 : 9, 81~87 or 8801~8806
● Dial the desired number.
Placing an Incoming Call
● Lift handset.
● Dial 3-digit intercom number.
Placing a Call on Hold (Exclusive Hold)
● While connected to an outside line, briefly press
and release the hook switch.
● To retrieve the call, briefly press and release
the hook switch again.
Placing a Call on Hold (System Hold)
● While connected to an outside line, briefly press
and release the hook switch.
● Dial 8.
● To retrieve the call held by itself, dial 8 *.
To Retrieve a Call on Hold
● Lift handset.
● Dial 8 9 (or 8 #) and line no.
(01-03 : 308A, 01-12 : 36, 01-14 : 46, 01-06 : 616)
To Transfer a Call to Internal Party
● While connected to an outside line, briefly press
and release the hook switch.
● Dial the station number to transfer.
● Hang up to complete call transfer.
(Or, hang up after you announce the called party
that a call is waiting.)
Flashing
Disconnects the present outside line and reseizes
dial tone from PSTN.
● While connected to an outside line, briefly press
and release the hook switch.
● Dial 7 5 1 and the phone number.
Last Number Redial
● Lift handset.
● Dial 7 5 0 . (or # # in GHX-616/36/46)
Group Call Pick-up
When hearing an unattended phone ringing in your
area,
● Lift handset.
● Dial * * .
● You will be connected to the incoming extension
or outside line call.

## Slide 2
Message Wait Indication
To leave a message wait indication,
● Dial intercom station number.
● Briefly press and release the hook switch.
● Dial 7 5 6 .
● Hang up.
To answer a message wait indication,
(This feature is allowed in GHX-36/46, and this can not
be used without Message Wait Unit)
● Lift handset.
● Dial 7 5 6 .
● The station that left message will ring.
Callback
To request callback,
● Dial busy intercom station number.(Busy tone is
heard.)
● Dial 7 5 6 .
● Hang up.
Conference
You may set up a conference of two external or internal station. (To set up a conference of two external lines, multi line conference should be enabled.)
● Place an outside call.
● Briefly press and release the hook switch and dial
7 5 2 .
● Dial the number of internal station you wish to add.
● When the station answers, briefly press and release
the hook switch again.
● Dial 7 5 2 .
Access Authorization Code
To prevent unauthorized outside call on your station by
others, the system provides user with means to lock/ unlock the station by Access Authorization Code.
● Lift handset.
● Dial 7 4 4 and enter 4 digits Access Authorization
Code (0000~9999).
● Hang up.
To change Access Authorization Code,
● Lift handset.
● Dial 7 4 5 .
● Enter your current access authorization code.
● Dial your new access authorization code.
● Hang up.
Blocking Outside Call
If your station has been registered,
● Lift handset.
● Dial 7 4 7 .
● Hang up.
Restoring Outside Call
If your station has been registered and locked,
● Lift handset.
● Dial 7 4 8 and access authorization code.
● Hang up.
Wake-up Call
The system automatically sends ring signal to the
station which registers wake-up time.
● Lift handset.
● Dial 7 4 1 (effective until canceled) or 7 4 2 (for
one-day).
● Enter 4-digit wake-up time (HHMM) in 24-hour
mode. (HH : 00~23, MM:00~59)
● Hang up.
To cancel wake-up call,
● Lift handset.
● Dial 7 4 3 .
● Hang up.
Universal Night Answer
When hearing an incoming signal on other phone or
night bell,
● Lift handset.
● Dial UNA Access Code 7 7 7 .
● You will be connected to an incoming call if it was
programmed as an UNA line.
Preselected Message
You can choose a preselected message to be displayed on the LCD of the phone calling your station.
● Lift handset.
● Dial 7 2 .
● Dial the following number to leave a message.
(01~20)
Message Type - I
0 0 : cancel the message
0 1 : OUT TO LUNCH
0 2 : ON VACATION
0 3 : OUT OF OFFICE - BACK AM
0 4 : OUT OF OFFICE - BACK PM
0 5 : OUT OF OFFICE - BACK TOM
0 6 : OUT OF OFFICE - BACK UNKN
0 7 : OUT OF TOWN
0 8 : IN A MEETING
0 9 : AT HOME
1 0 : AT BRANCH OFFICE
1 1~2 0 : Customized messages

## Slide 3
Message Type - II
(It is available for only GHX-36/46/616. You can select
Message Type I or II by programming.)
0 0 : cancel the message
0 1: Lunch, return at xx:xx (xx:xx : time (4 digits))
0 2 : vacation, return on xx:xx
(xx:xx : time or date (4 digits))
0 3 : Absent, return at clk xx:xx (xx:xx : time (4 digits))
0 4 : Absent, return at date xx:xx(xx:xx : date (4 digits))
0 5 : Out Of Office - Back Tom
0 6 : Call xxxx (max. 12 digits)
0 7 : In Office xxx (3 digits internal station number)
0 8 : Meeting clk xx:xx (xx:xx : time (4 digits))
0 9 : At Home
1 0 : At Branch Office
1 1~2 0 : Customized messages
● Hang up.
Paging (Only external page is available for GHX-308A)
● Lift handset.
● Dial the desired page zone number.
● Give your message in normal voice tone.
● Hang up to complete paging.
Page Zones
Call all zones : # 0 Call all internal zones : # 5
Internal zone 1 : # 1 External Page : # 6
Internal zone 2 : # 2
To answer page: # 7 (Dial ## in GHX-308A)
Name Display Program
● Lift handset.
● Dial 7 5 5 * and enter name code. (up to 7 characters)
● Make hook flash.
● Hang up.
(To erase name display, dial 755* and make hook flash.)
DND (Do Not Disturb)
● Lift handset.
● Dial 7 5 3 to make or remove DND.
(Confirmation tone is heard.)
● Hang up